## Slide 1: How the Brain Moves: Understanding Motion-Based Brain States Using Deep Learning Techniques
Joshua Tapper
Supervisor: Dr. Ignasi Cos
Universitat de Barclona
July 8th 2025

## Slide 2: Agenda 01 05 04 02 06 03
Present results of training analysis
Provide project motivation and explain data
Introduce our methods for feature attribution
Show how data was prepared for training
Offer final thoughts
Discuss the models and training methodology
Background
Interpretability
Results
Preprocessing
Conclusions
Training

## Slide 3: Background 01

## Slide 4: Motivation
Neural data can be very informative, but it is also highly-dimensional, non-linear, and noisy, making it difficult to understand.
Deep learning models can be trained on neural data to learn its complex patterns and achieve accurately classification.
After model training, we can extract input feature importance to better understand the input data and thus our brains.
Problem
Model Classification
Model Interpretability

## Slide 5: Data Source
Data comes from Local Field Potentials (LFPs)
  Invasive procedure to record electrical activity within the brain
  Higher spatial resolution on a smaller subset of the brain when compared to electroencephalograms (EEGs)
Notes: Invasiveness means we can capture wider range of frequencies
LFP data much less tested
Explain why we separate bands (associated with different levels of activity)

## Slide 6: Experiment Overview
Data comes from the experiment described in DePass et al., 2022.
In that experiment neural data is recorded while macaque monkeys perform a series of movements using both their left and right hands.
  Data is recorded on 256 channels from five regions of the brain: the left and right ventral premotor cortex (PMv), the left and right dorsal premotor cortex (PMd) and the left primary motor (M1).
We have in total 1575 samples and 9 classes from our data.
  Singular baseline class and separate classes per movement and hand.
Notes: Data comes from Montreal, was given to authors who work with UB
All five regions are associated with brain movement
  Dorsal – triggered by environmental cues
  Ventral – within reach objects

## Slide 7: Preprocessing 02

## Slide 8: Spectrograms
Data was transformed into spectrograms, which are visual representations of how frequency changes over time.
This allows us to use image analysis techniques to learn and classify the data.

## Slide 9: Data Cleaning
Two data cleaning methods were used:
Bad Channel Deletion – removes channels that are too flat or noisy when compared to the overall dataset.
Spectrogram Cleaning – Limits frequency values to cutoff artifact noise and deletes data around 60 Hz powerline spikes.

## Slide 10: Training 03

## Slide 11: Methodology Overview
Decoder
Models learns to represent data in a latent space
Classifier
Models learns to classify reduced data
Feature Attribution
Extract importance values of input features
Trained Together
01
02
03

## Slide 12: Encoder
The encoder reduces the channel dimension of the data from 245 to 32 while maintaining the spectrogram dimensions.
The architecture follows the Convolutional Autoencoder structure but does not include the decoder.
The encoder is combined with a classification model so that the decoder optimizes using the classification loss.
01
02
03

## Slide 13: CNN
01
02
03
The first classification architecture used was a Convolutional Neural Network (CNN). Two important characteristics of the CNNs used are:
Stacked convolutional layers, which allow for increased model discrimination while using smaller kernel sizes and thus less parameters. As an example:
  Two (3x3) kernels results in parameters
  One (5x5) kernel results in parameters
Asymmetric kernel shapes, such as (5x3), to account for our unbalanced spectrogram shape.
Notes: C represents channels of the stack

## Slide 14: CNN-LSTM
01
02
03
The second architecture builds upon the CNN architecture by adding two stacked Long Short-Term Memory (LSTM) layers.

## Slide 15: Parallel Model
01
02
03
The final classification architecture used is a Parallel CNN and LSTM model, which trains both architectures separately and concatenates the outputs.
Notes: Dropout is not shown
New or novel use case

## Slide 16: Training Strategy
01
02
03
All three model architectures had parameters optimized through a light Grid Search (a few hundred combinations per architecture).
All models used an Adam optimizer with the Sparse Categorical Crossentropy Loss.
The train/test split was 80%/20%.
Models were trained using Early Stopping and Learning Rate Decay.

## Slide 17: Interpretability 04

## Slide 18: SHAP
A game theory-based feature attribution approach that indicates how much an input feature impacts the prediction for a given class.
Two SHAP explainers were used:
  DeepExplainer (preferred method)
  KernelExplainer (problematic for our models)
01
02
03

## Slide 19: Integrated Gradients
Performs feature attribution using gradients, which compare how a feature changes the output when compared to a baseline image.
Integrated Gradients were calculated for 100 test samples per model and averaged to yield feature importance.
  A baseline black image was used.
01
02
03

## Slide 20: Ablation
01
02
03
In our case, ablation refers to setting the values of a set of input features to 0 and evaluating how that impacts the accuracy of trained models.
  “Importance” is then simply the loss in accuracy the ablated features cause.
Three manners of ablation were performed:
  Individual channel ablation
  Brain region ablation
  Frequency band ablation

## Slide 21: Results 05

## Slide 22: Training Methodology Comparison
Model | Data Cleaning | Dimensionality Reduction | Test Accuracy
CNN | Yes | Encoder | 75.2%
CNN-LSTM | Yes | Encoder | 83.2%
Parallel | Yes | Encoder | 82.2%
CNN | Yes | PCA | 74.6%
CNN-LSTM | Yes | PCA | 71.4%
Parallel | Yes | PCA | 71.7%
CNN | No | Encoder | 81.2%
CNN-LSTM | No | Encoder | 78.0%
Parallel | No | Encoder | 75.5%
CNN | Yes | None | 78.4%
CNN-LSTM | Yes | None | 77.1%
Parallel | Yes | None | 80.3%

## Slide 23: Problems with SHAP
Values of top channels are much lower than CNN values.
Many missing values implies many features were not tested at all.

## Slide 24
SHAP Importances
Integrated Gradient Importances

## Slide 25: Channel Ablation
The left PMd again shows clear top importances.
  We also still see the subregion of particularly high importance within the PMd.
  Accuracy increases suggest more aggressive bad channel deletion can be tested.

## Slide 26: Frequency Ablation
The multiunit band and high gamma bands cause the largest drops in accuracy.
The CNN-LSTM and Parallel models show a similar pattern but are less robust to multiunit ablation and more robust to the ablation of all other bands.

## Slide 27: Regional Ablation
The left PMd again shows high importance.
The right PMd causes surprisingly high accuracy drops given perceived lower importance using other methods.

## Slide 28: Confusion Matrix
There is lots of confusion between the baseline class and the pre-reach/post-grasp classes, especially the left-handed pre-reach class.
Models are more successful at predicting the reach and grasp stages.
Models are also generally better at right-handed predictions than left-handed ones.

## Slide 29: Conclusions 06

## Slide 30: Comparison with Di Croce’s Reservoir Computing
Reservoir computing achieved an 89% accuracy while classifying on 10 classes and using amplitude smoothing as additional preprocessing.
Di Croce found similar accuracies when training on all five regions. For frequencies, his results were best when training on the multiunit band, and second best when using the gamma and ripple bands.
Reservoir computing appears stronger in performance and robustness when it comes to predictions, but those qualities can make it more difficult for precise feature attribution.
Model Performance
Feature Importance
Overall Thoughts

## Slide 31: Future Ideas and Suggestions
Models can be further optimized through more expansive grid searches.
More testing can be done on spectrogram creation and data cleaning.
Models can be trained on specific regions and frequency bands to assess how much valuable information they contain.
SHAP provides feature importances per class, which could provide more insight in how different types of movement are signaled differently within the brain.

## Slide 32: Final Discussion
Our models prove that accurate multiclass classification using LFP data is possible.
The left PMd, multiunit band, and high gamma band are highly important for the prediction of movement.
The CNN-LSTM and Parallel architectures produced similarly strong results. An intramodel decoder can offer additional utility and outperforms methods like PCA.
SHAP, Integrated Gradients, and ablation all provide interesting insights. SHAP might be stronger than Integrated Gradients but has more limited use.
Training Results
Important Features
Model Architecture
Attribution Methods

## Slide 33: Thank You!
Code and full report of this project are available on GitHub. For any questions please contact:
jtappeta214@alumnes.ub.edu